Preflight

Interior

Mags - Off

Cowl flaps - Open

Fuel selector - Left tank

Gust lock - Remove

Landing gear switch - Down

Master switch - On

Fuel gages - Check quantity

Flaps - Down

Master switch - Off

Aircraft documents - ARROW

Weight and balance - Review

Flashlights/equipment - Check

Exterior

Empennage - Check security, movement, trim tab security/cable attachment free play

Tail tiedown - Remove

Right static port - Check unobstructed

Underside - Check condition, antennas

Right flap - Check for damage, security

Right aileron - Check for damage, security, movement

Right wing - Check for damage

Right tiedown - Remove

Right gear - Check strut (2 inches showing), uplock roller, brakes, and tire (30 psi)

Right fuel tanks -

Main gear - Check strut (2 inches showing) and tire (30 psi)

Preflight (cont’d)

Right cowl - Check secure

Cowl plugs - Remove

Propeller and spinner - Check condition

Engine air inlet - Check unobstructed

Left cowl - Open

Alternator belt - Check tension

Oil level - Check (9 quarts max. 8 quarts min.)

Oil filler cap - Check secure

Left cowl - Close

Fuel selector drain - Check sump

Left wing - Check for damage

Left fuel tanks - Check quantity, vents, sump

Left gear -.Check strut (2 inches showing), uplock roller, brakes, and tire (30 psi)

Pitot tube - Remove cover. Check for obstructions

Stall warning switch - Check movement, operation

Navigation lights (night flight) - Check

Left tiedown - Remove

Left aileron - Check for damage, security, movement

Left flap - Check for damage, security

Left static port - Check unobstructed

Starting Engine

Cold

Brakes - Set

Landing gear switch - DOWN

Circuit breakers - Check

Fuel - Desired tank (Left?, NEVER Aux)

Prop - Full increase

Mixture - Rich

Throttle - Open 2 turns

Master switch - ON

Fuel pump - LOW, wait until indication on fuel flow meter, then OFF

Prop area - ``Clear!’’

Starter - Engage

Engine speed - 1000 RPM

Fuel pump - OFF

Oil Pressure - must indicate within 30 seconds

Flaps - UP

Flap switch - Center

Beacon - ON

Hot

Same as cold, except...

Mixture - Rich

Throttle - Open 1 turn

Fuel pump - LOW - peak twice, then OFF

Throttle - Open 3/4 of full throttle

Prop area - ``Clear!’’

Starter - Engage

Fuel pump - LOW momentarily as engine fires

Throttle - Reduce immediately

After Start

Nav lights - On, as appropriate

Radio master - ON

Transponder - STANDBY

ATIS, Ground, Tower - SET                   (SQL 125.9/121.6/119.0)

Altimeter - Set (within 40’ field elev.)

Taxi

Brakes - Test

Artificial Attitude - Check operation

Turn Coordinator - Check operation

Directional Gyro - Check operation

Magnetic compass - Check operation, fluid level

Before Takeoff

Engine Runup

Brakes - Set

Fuel - Desired tank (left?). NEVER aux!

Mixture - Rich

Oil temperature - Wait for 70°F

Engine speed - 1800 RPM

Mags - Test: L-Both-R-Both. Drop-off < 100 Rpm and < 50 RPM differential..

Prop - Cycle twice full travel. Check oil pressure/man pres/RPM drop, normal return.

Vacuum - Between 4 - 7 inches

Alternator - Charging - show discharge

Instruments

Engine gages - Check

Instruments - Check and set

Mags - BOTH

Prop - Full increase

Mixture - Rich

Elevator trim - 3° (green/white transition)

Aileron trim- Neutral

Flaps - 0° (first line 10° short/soft field)

Flight controls - Free, correct, and smooth.

Door, shout, and emergency windows - Latched

Seat belts - Fastened

Passengers - Briefed

Navigation

Tower/Departure freq. - Set

Sqawk - Set

Departure route/Navaid - Set

Takeoff

Transponder - ALT

Mixture - Rich

Prop - Full increase

Strobes - ON

Landing lights - As appropriate

HSI - Check heading with runway number

Departure time - Record

Mixture - Lean for takeoff, if elevation > 3000 feet

Rotate - 60-70 mph, VX - 75 mph Vy - 103 mph (sea level)

Post Takeoff

Gear - UP (when out of usable runway)

Flaps - Up

Throttle/Prop - 1000 feet AGL, - 24’’/2400 RPM

Climb

Each cardinal 1000 feet - Adjust manifold pressure

Pass 3000/5000/7000 feet - Adjust mixture

Cruse

Throttle/Prop - Set for cruse

Mixture - Lean 50°F (25° if 65% power) below peak.

Cowl flaps - Close

Landing - Downwind

Gas Fuel - Proper tank (NOT aux)

Undercarriage Gear - DOWN (140 mph max)

Mixture - Full rich (sea level) or as appropriate

Prop - Full increase (after power reduction)

Switches/Seatbelts - Landing lights/Passengers briefed and belted

Flaps - Set (120 mph max)

Approach speed - 90 mph

Landing - Final

Prop - Full increase

Cowl flaps - Open

Gear - DOWN indicated locked

Speed over the fence - 80 mph

Go Around

Prop - Full increase

Throttle - Full power

Mixture - Rich (sea level) or as appropriate

Throttle - Full power

Flaps - Up gradually

Gear - UP

Cowl flaps - Open

Throttle/Prop - 1000 feet AGL - 24’’/2400 RPM

VX - 75 mph Vy - 103 mph

After Landing

Flaps - Raised

Transponder - STANDBY

Strobes - OFF

Shutdown

Radio master - OFF

Electrical Equipment - OFF

Throttle - 1000 RPM

Prop - Full increase

Mixture - Idle cut-off

Master switch - OFF

Mags - OFF

Arrival Time - Record

Secure

Flight time - Record in airplane log book

Elevator trim - 3° (green/white transition)

Cowl flaps - Close

Gust lock and bungee cords - Install

Instrument panel - Cover with towel

Cabin door - Close and lock

Airplane cover - Install

Pitot tube cover - Install

Cowl plugs - Install

Tail and wing tiedowns - Secure

Flight plan - Close

EMERGENCY Gear Extension

Master switch - ON

Gear - DOWN

Gear indicator - Check green lamp lit or lower indicator in the DOWN position.

If gear down indication still not present:

Airspeed - < 120 mph

Gear circuit breaker - Pull

Gear crank - approx. 50 counterclockwise turns

Lower gear indicator - Verify in down position

Gear crank - Stow

Note: with landing gear circuit breaker “pulled”, landing gear position lights are nonfunctional.

EMERGENCY Gear Up Landing

In an emergency, a gear up landing may be made:

When the surface is too soft or rough to permit a satisfactory gear down landing.

When a field is too short for a gear down landing, one that might cause more damage by hitting obstructions than a gear up landing would.

When a water landing is necessary.

Flaps - UP

Throttle - CLOSED

Master - OFF

Mags - OFF

Fuel selector - OFF

EMERGENCY Power Loss

Best glide speed - 103 mph

Select suitable landing area

Fuel selector - Switch to tank not in use

Throttle - Open 1/2 inch from present setting

Prop - Full increase

Fuel pressure - Check. If none, Fuel pump - HIGH

Mags - Check best: left, right, both.

To restart failed engine:

Fuel pump - OFF

Throttle - Closed

Mixture - Idle cut-off

Fuel selector - OFF

Wait several seconds

Fuel elector - Fullest tank

Mixture - Rich

Throttle - Open 1/4 inch

Fuel pressure - If zero - Fuel pump - HIGH

If engine cannot be restarted:

Mixture - Idle cut-off

Throttle - Closed

Mags - OFF

Fuel selector - OFF

Prop - Low RPM

Best glide speed - 90 mph

EMERGENCY Engine Fire In Flight

Mixture - Idle Cut-off

Fuel selector - OFF

Mags - OFF

Throttle - Closed

Best glide speed - 103 mph